## Slide 1: Addison Airport (ADS) Runway Incursion Risk Areas
Runway 15-33 and Taxiway Alpha have less than the FAA standard (400-ft.) separation
Holding positions east of Rwy 15-33 were moved in late 2002 to comply with current FAA standards; they are unusually close to Twy Alpha!
Pilots holding short of Rwy 15-33 must maintain awareness of the proximity of the mandatory hold position line…this has been the site of several Pilot Deviations over the past few years!
Pilots: pay close attention to hold line locations and ATC instructions!
Juliet
Alpha
Alpha
Runway 15
300 ft.
250 ft.
Holding positions very close to Taxiway Alpha
DO NOT cross hold lines without ATC clearance!!

## Slide 2: Addison Airport (ADS) Runway Incursion Risk Areas
300 feet
250 feet
Rwy 15-33
Twy Alpha
Runway 15-33 and Taxiway Alpha have less than the FAA standard (400-ft.) separation
Holding positions east of Rwy 15-33 are unusually close to Twy Alpha
Aircraft holding short of Rwy 15-33 may block traffic on Twy Alpha; this is OK, ADS Ground is aware of the situation and compensates for it
Aircraft clearing Rwy 15-33 must taxi past the hold lines onto Twy A unless otherwise instructed by ATC
Pilots: pay close attention to hold line locations and ATC instructions!
vehicle service roadway
hold line